## Slide 1
High resolution seismic imaging:
Asymptotic approach
By Jean Virieux
Professeur
UGA
American Petroleum Institute, 1986
Salt Dome
Fault
Unconformity
Pinchout
Anticline

## Slide 2: Time scales
Source time
from 0.1 sec to 100 sec (rupture vel.)
Wave time
from secondes to hours
Window time
from few secondes to days

## Slide 3: Length scales
Fault length
200 km for vr=2 km/s
Discontinuity distance
from few meters to few 100 kms
Volume sampling
from few kms to few 1000 kms

## Slide 4: Examples
Record of a far earthquake (Müller and Kind, 1976)
Traces from a oil reservoir (Thierry, 1997)
Records on the Moon (meteoritic impact) (Latham et al., 1971)
Seismic imaging is a tough problem on the Moon !

## Slide 5: Motivation
Delayed travel-time tomography source:receiver
  Fitting times => estimation of times
  => 2-pts rays: millions!
Full Waveform Inversion/Migration src/rec:focal point
  Same challenge with an order increase in magnitude
Seismogram modeling
  Handling multiple arrivals and filling gaps (shadows)
Rays  Geometrical Optics Infinite Frequency Singularities topology
A link with the Catastrophe Theory (René Thom)
Do we need this complexity?

## Slide 6: FWI: Ray+Born approach
Ray tracing efficient only in smooth media
Updating the velocity structure through iterations induces a dramatic increasing complexity in ray tracing: people stays often (always) with the initial ray tracing once done (Background model~Born)
Asymptotic theory (or high frequency approximation) introduces a complexity in our finite frequency seismic wave propagation : all scales are there while they are not present in the seismic data
In fluid mechanism:
physics below a given small scale is parametrized (upscaled)

## Slide 7: References
Červený, V., Seismic ray theory, Cambridge University Press, 2001
Chapman, C., Fundamentals of seismic wave propagation, Cambridge University Press, 2004
Slawinski, M.A., Seismic waves and rays in elastic media, Handbook of geophysical exploration, seismic, exploration, volume 34, Pergamon, 2003
Abdullaev, S.S., Chaos and dynamics of rays in waveguide media, Gordon and Breach Science Publishers, 1993
Goldstein, H, Classical mechanics, Addison-Wesley Publishing company, second edition,1980
Glassner, A.S. (editor), An introduction to ray tracing, Academic Press, second edition, 1991
Gilmore, R, Catastrophe theory for scientists and engineers, Wiley & Sons, Inc, 1981.
Sethian, J.A., Level Set Methods and Fast Marching Methods: Evolving Interfaces in Computational Geometry, Fluid Mechanics, Computer Vision, and Materials Science, Cambridge University Press, 1999.
Virieux, J. and Lambaré, G., Theory and Observations-Body waves: Ray methods and finite frequency effecs in Treatrise on Geophysics, Tome I by A. Diewonski and B. Romanowicz, Elsevier, 2010

## Slide 8: References (selection)
Červený, V., Seismic ray theory, Cambridge University Press, 2001
Chapman, C., Fundamentals of seismic wave propagation, Cambridge University Press, 2004

## Slide 9
Translucid Earth
Diffracting medium:
wavefront coherence lost !
Wavefront preserved
Wavefront : T(x)=T0
Travel-time T(x) and Amplitude A(x)
Source
Receiver
Same shape !
T(x)
S(t)
is sometimes called the phase

## Slide 10: Eikonal equation
Two simple interpretations of wavefront evolution
Orthogonal trajectories are rays in an isotropic medium
Grad(T)= orthogonal to wavefront
Direction ? : abs or square
The orientation of the wavefront could not be guessed from the local information on a specific wavefront
T+DT
T=cte
Velocity c(x)
DL
Ray
10

## Slide 11: Transport Equation
Tracing neighboring rays defines a ray tube : variation of amplitude depends on energy flux conservation through sections.
Energy flux same at section one and at section two
net contribution=zero

## Slide 12
Ray equation
Ray
T=cte
Evolution of is given by
but the operator
and, therefore,
leading to
Evolution of is given by
Wavefront
Ray equations
We define the slownss vector and the position along the ray
Curvature equation

## Slide 13: Various non-linear ray equations
Which ODE to select for numerical solving ? Either t or x sampling.
Many analytical solutions (gradient of velocity; gradient of slowness square)
Curvilinear stepping
Particule stepping
Time stepping
under the condition of the eikonal
The simplest set

## Slide 14: How to solve these equations ODE versus PDE !

## Slide 15: ODE Lagrangian formulation Wavefront complexity

## Slide 16: Methods of characteristics
Differential geometry (Courant & Hilbert, 1966)
Non-linear ordinary differential equations
Lagrangian formulation as we integrate along rays
In opposition to Eulerian formulation where we compute (ray) quantities at fixed positions

## Slide 17: Properties of these ODEs
Intrinsic solutions independent of the coordinate sytem used to solve it
If dummy variable for velocity, use it as the variable stepping (often x coordinate)
(1)
Eikonal equation: a good proxy for testing the accuracy of the ray tracing (not enough used)
In 3D: six or seven equations
In 2D: four or five equations
(1): rectilinear motion of a particle along this axis in mechanics

## Slide 18: Hamilton’s ray equations
Information around the ray
Ray
Mechanics : ray tracing as a particular balistic problem
sympletic structure (FUN!)
Meaning of the neighborhood zone
Fresnel zone if finite frequency
Any zone depending on your problem GBS
Hamilton approach suitable for perturbation
(Henri Poincaré en 1907 « Mécanique céleste »,
Richard Feymann Prix Nobel 1965)

## Slide 19: Velocity variation v(z)
Ray equations are
The horizontal component of the slowness vector is constant: the trajectory is inside a plan which is called the plan of propagation. We may define the frame (xoz) as this plane.
Where px is a constante
For a ray towards the depth

## Slide 20: Velocity variation v(z)
At a given maximum depth zp, the slowness vector is horizontal following the equation
zp
If we consider a source at the free surface as well as the receiver, we get
In Cartesian frame
In Spherical frame
with p = usini

## Slide 21: Velocity structure in the Earth
Radial Structure

## Slide 22: System of ray tracing equations
Which ODE to select for numerical solving ? Either t or x sampling.
Many analytical solutions (gradient of velocity; gradient of slowness square)
Curvilinear stepping
Particule stepping
Time stepping
under the condition of the eikonal
The simplest set

## Slide 23: Time integration of ray equations
Initial conditions EASY
1D sampling of 2D/3D medium : FAST
source
receiver
Runge-Kutta second-order integration
Predictor-Corrector integration
stiffness
source
receiver
Boundary conditions VERY DIFFICULT
?
?
Shooting dp ?
Bending dx ?
Continuing dc ?
AND FROM TIME TO TIME IT FAILS !
But we need 2 points ray tracing because we have a source and a receiver to be connected in seismology!
Save p conditions if possible !

## Slide 24
Ray tracing
Constant angle step
Ray tracing by rays

## Slide 25
Two-point ray tracing
Ray tracing by rays
Source (0,0)
Receivers (2,-2),
(4,-2),(6,-2)
(depth is considered as negative)
Please note the irregular angle stepping.

## Slide 26: Hamilton’s ray equations
Information around the ray
Ray
Mechanics : ray tracing as a particular balistic problem
sympletic structure (FUN!)
Meaning of the neighborhood zone
Fresnel zone if finite frequency
Any zone depending on your problem GBS
Hamilton approach suitable for perturbation
(Henri Poincaré en 1907 « Mécanique céleste »,
Richard Feymann Prix Nobel 1965)

## Slide 27: ODE resolution
Runge-Kutta of second order
Write a computer program for an analytical law for the velocity: take a gradient with a component along x and a component along z
Home work : redo the same thing with a Runge-Kutta of fourth order (look after its definition)
Consider a gradient of the square of slowness

## Slide 28: Analytical solutions
Vertical gradient of the velocity
Gradient of the slowness square

## Slide 29: Keeping complexity low
Ray tracing is a fast 1D integration in 2D/3D
Ray tracing equations as ODEs may sample the medium quite evenly
They are lagrangian formulation: we follow a point while tracing rays without regarding the density of rays

## Slide 30: Keeping complexity low
Solutions: moving from ODEs to PDEs
(Osher et al, 2002) for adequate spatial sampling of the wavefront. Grids control the complexity!
3D French’s model

## Slide 31: Interpolation challenge

## Slide 32: Mitigating the interpolation issue
We cannot guarantee that two rays will stay nearby for small shooting angles changes
Differential approach will be an answer: the perturbed ray will stay nearby the reference ray …

## Slide 33: Hamilton’s ray equations
Information around the ray
Ray

## Slide 34
(Lambaré et al., 1996)
STEP ONE: ray tracing

## Slide 35: Local ODE Semi-Lagrangian approach Sampling control

## Slide 36: Ray tracing by wavefronts
Evolution over time:
folding of the wavefront is allowed (still a significant curse of complexity!)
Dynamic sampling:
undersampling of ray fans
oversampling of ray fans
Keep an « uniform » sampling of the medium by rays
by tracking the surrounding density of rays
by estimating through paraxial approach the ray density
Lambaré et al (1996)
Vinje et al (1993) widely used in NORSAR software
How to compute multiple arrivals?
(Ray tracing by rays)

## Slide 37
Rays and wavefronts in an homogeneous medium.
(Lambaré et al., 1996)
Ray tracing by wavefronts
An ODE is solved at each point of the wavefront while it is spanned
Keeping the sampling of the medium more or less uniform

## Slide 38: Ray tracing by wavefronts
Sampling the wavefront is an heavy task in 2D & 3D !
Still better than oversampling through ray tracing by rays
Example of wavefront evolution in a smooth version of the Marmousi model
Smoothness is required !
How to compute multiple arrivals?

## Slide 39
(Runbord, 2007)

## Slide 40: Geometrical optics resolution
No scale as we are at infinite frequency !
Is it a fair assumption while we have finite frequency wave content?
We must proceed down to a given resolution length under which we do not want to decipher the wavefront: wavefront healing related to so-called viscous solution.
Do we need this complexity of tracking seismic wavefronts!

## Slide 41: Few attempts
The medium should be smooth enough for avoiding the wavefront tracking …
Usually done once in the initial model when performing imaging procedure …
A better strategy? Yes, for first arrivals; maybe for multiple arrivals.

## Slide 42: PDE Eulerian approach Grid control

## Slide 43: Level-set functions
Eikonal equation
The eikonal equation is a first-order non-linear partial differential equation of static Hamilton-Jacobi equations: Crandall & Lions (1983, 1984) have shown that « viscous » solutions of such equation can be obtained.
« Computing first-arrival times is equivalent to tracking an interface advancing at a local speed normal to itself » from Sethian & Popovici (1999)
Level-set methods (Osher & Sethian, 1988)
Fast marching methods (Sethian, 1996a; Sethian and Popovici, 1999)
Fast sweeping methods (Zhao, 2005)
Discontinuous Finite-Element methods (Li et al, 2008; Yan & Osher, 2011)
Using an upwind, monotone and consistent discretization of

## Slide 45: Eikonal Solvers Fast marching method (FMM)
(tracking interface/wavefront motion : curve and surface evolution)
In a 2D layered medium
Let us assume T is known at a level z=cte
z=cte
z
z + dz
Compute along z=cte by a finite difference
approximation
Deduce from eikonal
From T at a depth of z, we have been able to estimate T at a depth of z+dz
EIKONAL SOLVER
ONLY FIRST-ARRIVAL!
a)
b)
c) down
Extend T estimation at depth z+dz

## Slide 46: Fast marching method (FMM)
Computing T(x,z) is a stationay boundary problem: discretize it on a grid and find an efficient numerical method to solve it.
2D case
The solution is updated by following the causality in a sequential way: updated pointwise in the order the solution is strictly increasing (upwind difference scheme and a heap-sort algorithm)
Sharp interfaces are difficult to describe
From Sethian & Podovici (1999)
where N is the number of grid points in a direction

## Slide 47: The ENO or WENO stencil
How to estimate the discrete ?
A first-order Godunov upwind difference scheme
High-order improved ENO or WENO stencils (Liu et al, 1994; Jiang and Shu, 1996)
See Sethian’s book (1999)
with and
and with or

## Slide 48: Fast sweeping method (FSM)
Gauss-Seidel iterations with alternating direction sweepings are incorporated into same upwind finite difference stencil: complexity in
2D case
Velocity
Travel time
In 2D at least four sweeps are needed and six sweeps in 3D
Iterations are independent of the grid size
Singularities at the boundary may induce errors, especially for a point source (Luo & Qian, 2010)
From Zhao (2005)
Any mesh could be used
Computing T(x,z) is a stationay boundary problem

## Slide 49: Fast sweeping method (FSM)
2D case
Any mesh could be used
Waves travel along AC or BC direction with an apparent slowness which is the projected slowness value from the true slowness vector.
Han et al (2015)
Quadratic equation: real solution needed!

## Slide 50: Causality and viscosity
2D case
P
IF unset and IF unset, do nothing
IF set and IF unset, compute as if wave comes from A
IF unset and IF set, compute as if wave comes from B
IF set and IF set, do
compute roots of equation (1)
if real solution
check if the « backward ray » intersects the segment [AB]
if yes, update by this value if it is smaller
if no real solution, compute the viscous solution
as wave is coming from A or from B: select the smallest value
enddo
equation (1)
A
B
C
We provide always a value if A and/or B have a value
# ray tracing

## Slide 51: Fast sweeping method (FSM)
2D case
Eight points stencil:
From the possible eight values (if one is set), take the smallest one.
Sweeping technique:
Four sweeping when applying the stencil
Sweep 1: ;
Sweep 2: ;
Sweep 3: ;
Sweep 4: ;
Iteration over sweeps until convergence
(no more updating of )
We need to setup a set of values which will be fixed:
at the source, , for example

## Slide 52: Number of iterations
The number of iterations depend on the medium structure: one must be aware that the characteristics of the hyperbolic system should be sampled at least once by the sweeping loop.
In seismics or seismology, we have less dramatic configuration than the one shown in this figure
Few iterations are necessary to achieve convergence

## Slide 53: 2D examples
See Taillandier et al (1999) for an application to first-arrival time tomography using the adjoint formulation
(Luo and Qian, 2008)
A smooth model constructed from Marmousi
Wavefronts as deduced from travel-time computation
Only first-arrival times

## Slide 54: 3D example
Zhang, Zhao and Qian (2005)

## Slide 55: Drawback: only first-arrival times!
Time over the grid
Ray
Once traveltime T is computed over the grid for one source, we may backtrace using the gradient of T from any point of the medium towards the source (should be applied from each receiver)
The surface {MIN TIME} is convex as time increases from the source : one solution !
Back to inversion through rays
Still very usefuf to back-raytracing once we know times: getting the Jacobian matrix
Could we do better: multi-arrival times and amplitudes?

## Slide 58
(Runbord, 2007)
X
X

## Slide 59: Time error over the grid (0)
NOT THE SAME COLOR SCALE (factor 100)
Coarser grid for computation
Errors through FMM times
Errors through rays deduced after FMM times

## Slide 60: Conclusion Rays and Waves
Geometrical optics: ODE versus PDE
  Choose PDE when possible !
ODE: tracing one (paraxial) ray is fast
  Please trace paraxial rays as incremental cost
Keep complexity low (seismic waves are finite frequency waves)
  Do not drown yourself into the no-scale optical singularities
Identification of rays is a key problem
  PDE seems to solve it explicitly !

## Slide 61: Perspectives Rays and Waves
Fast sweeping method O(N) for travel-times and for amplitudes
  Amplitude equations have been designed
Finite element methods put into the scene
  Stencils are moving to higher orders and h-adaptivity
Discontinuous Galerkin methods
  This is the road to take for interface investigation in the frame of PDE.

## Slide 62
Inverse problem
Jean Virieux
Year 2015-2016
1
Other inverse problems?
From Brossier (2013,2014)

## Slide 63: Few hints

## Slide 64: Least-square method
Sum of vertical distances between data points and expected y values from the unknown line y=ax+b should be minimum: find a and b?
From Excel
It is an inversion ….

## Slide 65: Occam’s razor
Do not use more complicated maths than the data deserves
Approximate the least constrained quantity
Given: data (observed and modeled)
Assumed: wave propagation
Unknown: Earth structure
Occam’s Razor: parcimonious principle
When you have many explanations for predicting exactly the same quantities and that there is no way to distinguish them, select the simplest one… until you end up with a contradiction.
Ockham (~1295-~1349)

## Slide 66: Approximations can’t be avoided …
Incomplete data
Limited understanding
Limited crunching capacity
Limited frequency range: translucid Earth
Limited dataset: direct access impossible (or difficult)
Data windowing (observables): extraction of robust information
Dimensionality (2D vs 3D …)
Structural complexity (multi-scale heterogeneities)
Physics approximation (elastic vs acoustic)
« An approximate solution to a real problem is better than an exact solution to an ideal problem » (Tarantola, 2007)

## Slide 67
From Nissan-Meyer (Oxford)

## Slide 68: How to reconstruct the velocity structure ?
Forward problem (easy)
from a known velocity structure, it is possible to compute travel times, emergent distance and amplitudes.
Inverse problem (difficult)
from travel times (or similarly emergent distances), it is possible to deduce the velocity structure : this is the time tomography
even more difficult is the diffraction tomography related to the waveform and/or the preserved/true amplitude.

## Slide 69: Tomographic approach
Very general problem
medicine; oceanography, climatology
Difficult problem when unknown a priori medium (travel time tomography)
Easier problem if a first medium could be constructed: perturbation techniques can be used for improving the reconstruction (delayed travel time tomography)

## Slide 70: Travel Time tomography
We must « invert » the travel time or the emergent distance for getting z(u): we select the distance.
Abel problem (1826)
Determination of the shape of a hill from travel times of a ball launched at the bottom of the hill with various initial velocity and coming back at the initial position.

## Slide 71: ABEL PROBLEM
A point of mass ONE and initial velocity v0 reaches a maximal height x given by
We shall take as the zero value for the potential energy: this gives us the following equations and its integration:
We may transform it into the so-called Abel integral
where t(x) is known and f(x) is the shape
of the hill to be found: this is an
integrale equation.
ds
dx
x
y
x

## Slide 72: The exact inverse solution
We multiply and we integrate
We inverse the order of integration
We change variable of integration
We differentiate and write it down the final expression

## Slide 73: THE ABEL SOLUTION
By changing variable x in a-x and x in a-x, we get the standard formulae
We must have
t(x) should be continuous,
t(0)=0
t(x) should have a finit derivative with a finite number of discontinuities.
The most restrictive assumption is the continuity of the function t(x).

## Slide 74: The solution HWB : HERGLOTZ-WIECHERT-BATEMAN
In Cartesian frame
In spherical frame
From the direct solution, we can deduce the inverson solution
After few manipulations, we can move from the Cartesian expression towards the Spherical expression
We find r(v) as a value of r/v

## Slide 75: Stratified medium
When considering discontinuities, ABEL/HWB method based on first arrival times has not an unique solution.
More over there will be an ambiguity when the velocity decreases (can only defined the velocity jump in this zone)
In fact, we avec an infinity of solutions when considering only direct and refracted waves.
We may find interfaces when considering all waves (including reflection waves)

## Slide 76: Triplication & shadow zone
Increase of the velocity: triplication and retrograde branch
Decrease of the velocity: shadow zone (and a retrograde branch)

## Slide 77: Shadow zone in the Earth
Abrupt decrease of velocity at the CMB (2900 km)
(Oldham, 1906, Gutenberg, 1912)

## Slide 78: Identify phases ?

## Slide 79: Identify phases ?
Draw the SS phase?

## Slide 80: Picking time ?
Onset time for first-arrival phases?
Times, phase and polarity readings iPc

## Slide 81: Picking time ?
Deciphering the waveform

## Slide 82: Low-pass or band-pass signals
Time picking accuracy is crucial as well as uncertainty estimation
East
North
Up

## Slide 83: Local shots
Picking onset times
Profile 70.5 m
Geophone distance 1.5 m
Shot 57 m
Water ponds below parking !

## Slide 84: Phase signature
P : mantle P wave
S : mantle S wave
K : Outer core P wave
I : Inner core P wave
J : Inner core S wave
c : Reflected P wave
(outer core)
i : Reflected P wave
(inner core)
m : number of reflections
Please, describe the wave with signature
PKP, PKKP, SKKKS=S3KS

## Slide 85: Velocity structure with depth
Velocity profile built without any a priori
An difficulty arises when the velocity decreases.

## Slide 86: An initial model through the HWB method
An initial model can be built
The exact inverse formulae does not allow to introduce additional information,
F. Press in 1968 has preferred the exhaustive exploration of possible profiles (5 millions !). The quality of the profile is appreciated using a misfit function as the sum of the square of delayed times as well as total volumic mass and inertial moments well constrained from celestial mechanics ...
Exploration through grid search, Monte Carlo search, simulated annealing, genetic algorithm, tabou method, hant search and so on…

## Slide 87: The symmetrical radial EARTH

## Slide 88: Time tomography
Only for one dimension … uptonow
What can we do in 2D, 3D and 4D?

## Slide 89: A simple case : small perturbation
Initiale structure of
velocity
Search of small variation
of velocity or slowness
Linear approach

## Slide 90: Example: Massif Central

## Slide 91: GLOBAL Tomography
Velocity variation at a depth of 200 km : good correlation with superficial structures.
Velocity variations at a depth of 1325 km : good correlation with the Geoid.
Courtesy of W. Spakman

## Slide 92: Delayed Travel-time tomography
Consider small perturbations of the slowness field
Finding the slowness u(x,y,z) from t(s,r) is a difficult problem: only techniques for one variable u(z) (Abel) !
LINEARIZED PROBLEM
from the model domain to the data domain
« frozen » ray approximation
(ray connecting source/receiver for the known slowness

## Slide 93: Discretization of the slowness perturbation
The velocity perturbation field (or the slowness field) can be described into a meshed cube regularly spaced in the three directions.
For each node, we specify a value . The interpolation will be performed with functions as step functions. For each grid point (i,j,k), shape functions for i,j,k, and zero for other indices.
Nodal approach
Other shape functions are possible with two end members (nodal versus global):
fourier functions (cos,sin), chebychev, spline … and so on

## Slide 94: Discrete Model Space
Discretization of the medium fats the ray
Weighted ray segment
Sensitivity matrix J is a sparse matrix
also named Fréchet derivative or Jacobian matrix …
To be solved in least squares sense

## Slide 95: Joint hypo-velocity inversion
=

## Slide 96: Linear system
Slowness perturbation description
Matrice of sensitivity or of partial derivatives
Discretisation of the medium fats the ray
Sensitivity matrice is a sparse matrice

## Slide 97: Linear algebra

## Slide 98: Least-squares solution
The rectangular system can be recast into a square system (sometimes called normal equations).
Solving this square linear system gives the so-called least-squares solution.
Another interesting solution
The system is both under-determined and over-determined depending on the considered zone (and the number of rays going through.
Least-squares solution
Least-norm solution
Remark

## Slide 99: LINEAR INVERSE PROBLEM
Updating slowness perturbation values from time residuals
Formally one can write
with the forward problem
Existence, Uniqueness, Stability, Robustness
Discretisation
Identifiability
of the model
Small errors propagates
Outliers effects
NON-UNIQUENESS & NON-STABILITY : ILL-POSED PROBLEM
REGULARISATION : ILL-POSED -> WELL-POSED

## Slide 100: Weighted least-squares problem
Suppression of small eigenvalues by introducting a damping parameter
Least-norm solution
Remark
The damping parameter provides stable inverse
Tikhonov term with a Laplacian D

## Slide 101: More theory
For better understanding the influence of the damping parameter and the tikhonov term
Resolution matrix & Importance matrix

## Slide 102: LEAST SQUARES METHOD
L2 norm
locates the minimum of E
normal equations
if exists
Least-squares estimation
Operator on data will derive a new model : this is called
the generalized inverse
G0 is a N by M matrice
is a M by M matrice
Under-determination M > N
Over-determination N > M
Mixed-determination – seismic tomography

## Slide 103: SVD analysis for stability and uniqueness
SVD decomposition :
U : (N x N) orthogonal Ut=U-1
V : (M x M) orthogonal Vt=V-1
L : (N x M) diagonal matrice Null space for Li=0
UtU=I and VtV=I (not the inverse !)
Vp and V0 determine the uniqueness while Up and U0 determine the existence of the solution
Up and Vp have now inverses !

## Slide 104: Solution, model & data resolution
The solution is
where Model resolution matrice : if V0=0 then R=VVt=I
where Data resolution matrice : if U0=0 then N=UUt=I
importance matrice
Goodness of resolution
SPREAD(R)=
SPREAD(N)=
Spreading functions
Good tools for quality estimation

## Slide 105: Maximum Likelihood method
One assume a gaussian distribution of data
Data distribution could be written
where is the data mean and Cd is the data covariance matrice.
This method is very similar to the least squares method where we define the following misfit function .
Even without knowing the matrice Cd, we may consider data weight Wd through the misfit function
The inferred model distribution will be gaussian with the main difficulty of estimating the posterior model covariance connected with the curvature of the misfit function .

## Slide 106: PRIOR INFORMATION
Hard bounds
Prior model
The parameter is the damping parameter controlling the importance of the model mp
Gaussian distribution
Model smoothness
Penalty approach
add additional relations between model parameters (new lines)
with Wd data weighting and Wm model weighting
Seismic velocity should be positive

## Slide 107: Weighted Joint hypo-velocity inversion
=
Penalty strategy: add lines to the linear system to be solved

## Slide 108: L curve
Estimating the parameter is always difficult
We can test different values which provide a L curve
If a knee appears, this could be an adequat value … although this knee is often difficult to identify in seismic tomography.
Other techniques are available as LASSO approach but they are intensive and sensitive to noise.

## Slide 109: UNCERTAINTY ESTIMATION
Least squares solution
Model covariance : uncertainty in the data
curvature of the error function
Sampling the misfit function around the estimated model:
often this has to be done numerically
Uncorrelated data

## Slide 110: A posteriori model covariance matrice
True a posteriori distribution
Tangent gaussian distribution
S diagonal matrice eigenvalues
U orthogonal matrice eigenvectors
Error ellipsoidal could be estimated
WARNING : formal estimation related to the gaussian distribution hypothesis
If one can decompose this matrice

## Slide 111: A priori & A posteriori information
What is the meaning of the « final » model we provide ?
acceptable

## Slide 112: Local Newton methods
Steepest Gradient method
Conjugate gradient
Newton
Quasi-Newton
Gauss-Newton is Quasi-Newton for L2 norm
quadratic approximation of E

## Slide 113: LSQR method
The LSQR method is a conjugate gradient method developped by Paige & Saunders
Good numerical behaviour for ill-conditioned matrices
When compared to an SVD exact solution, LSQR gives main components of the solution while SVD requires the entire set of eigenvectors
Fast convergence and minimal norm solution (zero components in the null space if any)

## Slide 114: Linearized Inverse Problem
No explicit evaluation of the Hessian :
only products « » and « » are required in LSQR algorithm
Paige & Sanders (1982)
Misfit function
First loop over models : for current model (iteration k)
  Forward problem
    Solve eikonal equation
    Compute rays and synthetic travel-times
  Build Fréchet derivative matrix and delayed times
Second loop over linear system: iteratively solve
using conjugate gradient (LSQR, for example)
Update the model
Two-loops procedure

## Slide 115: Flow chart
true ray tracing
data residual
sensitivity matrice
model update
new model
collected data
starting model
loop
Calculate for formal uncertainty estimation
small model variation or small errors exit

## Slide 116
Initial velocity model
Ray tracing (src/rec)
Sensitivity matrix
(accurate synthetic delayed times dt)
LSQR iterative method
Outer loop
l
Err<eps
End
Inner loop
(70% of CPU)
Linearized Inverse Problem
Two-loops procedure
The slowness field is denoted by s and it is often the one we reconstruct

## Slide 117: Linearized Inverse Problem
Misfit function
First loop over models : for current model (iteration k)
  Forward problem
    Solve eikonal equation
    Compute rays and synthetic travel-times
  Build Fréchet derivative matrix and delayed times
Second loop over linear system: iteratively solve
using conjugate gradient (LSQR, for example)
Update the model
Two-loops procedure
Complexity: for forward/adjoint formulation and for gradient storage (: sparsity )

## Slide 118: Linearized Inverse Problem
Misfit function
Two-loops procedure
Complexity: for eikonal formulation
for back-ray tracing
for sensitivity matrix storage J
The sparsity is expressed through with only few points of the grid involved for each data

## Slide 119: Linearized Inverse Problem
Misfit function
First loop over models : for current model (iteration k)
  Forward problem
    Solve eikonal equation
    Compute synthetic travel-times and delayed times
  Adjoint problem
    Solve adjoint equation
    Build gradient
Descent method (steepest gradient or conjugate gradient or l-BFGS)
Update the model
(Sei & Symes, 1994; Leung & Qian, 2006; Taillandier et al, 2009)
One-loop procedure
No explicit evaluation of the Hessian
l-BFGS provides an evaluation of the H-1 from previous stored gradients

## Slide 120: Sampling a posteriori distribution
Resolution estimation : spike test
Boot-Strapping
Jack-kniffing
Natural Neighboring
Monte-Carlo sampling
Checker-board test

## Slide 121: Sampling a posteriori distribution
Uncertainty estimation for P and S velocities using boot-strapping techniques

## Slide 122: Coverage influence
Perturbation is spread along rays, coverage is important to constrain the inversion

## Slide 123: Ray approximation
Line
Volume
is the sensitivity kernel

## Slide 124: Ray approximation reasonnable approximation
Same gradient once estimated
on the model discretization grid
Gradient

## Slide 125: Applications

## Slide 126: Corinth Gulf
An extension zone where there is a deep drilling project.
How this rift is opening?
What are the physical mechanisms of extension (fractures, fluides, isostatic equilibrium)
Work of Diana Latorre
and of Vadim Monteiller

## Slide 127: Seismic experiment 1991 (and one in 2001)

## Slide 128: MEDIUM 1D : HWB AND RANDOM SELECTION

## Slide 129: Velocity structure image
Horizontal sections
Basin structure
Fast variation

## Slide 130: Velocity structure image
Vertical sections
P
S

## Slide 131: Resolution matrix
Workflow:
On the expected final solution, perform a small spike perturbation and invert for the synthetic new dataset
One line of the resolution matrix

## Slide 132: Vp/Vs ratio: fluid existence ?
Recovered parameters might have diferent interpretation and the ratio Vp/Vs has a strong relation with the presence of fluids or the relation Vp*Vs may be related to porosity

## Slide 133: Other methods of exploration
Grid search
Monte-Carlo (ponctual or continuous)
Genetic algorithm
Simulated annealing and co
Tabou method
Natural Neighboring method

## Slide 134: Conclusion FATT
Selection of an enough fine grid
Selection of the a priori model information
Selection of an initial model
FMM and BRT for 2PT-RT
Time and derivatives estimation
LSQR inversion
Update the model
Uncertainty analysis (Lanzos or numerical)

## Slide 135
Dramatic increase of acquisition density both in the academic world (increasing density and in the industrial world (continuous recording)
General trend
for
seismic tomography

## Slide 136: IRIS DATA CENTER

## Slide 137: THANK YOU !
http://seiscope.oca.eu

## Slide 138: THANK YOU !
Many figures have come from people I have worked with:
many thanks to them !

## Slide 139: Delayed Travel-time Tomography
Still DTT provides impressive images while we do believe that DFT would provide better images in the future, thanks to finer discretization coming with the densification of the available data.
(Li & van der Hilst, 2010)
Delayed Fresnel Tomography

## Slide 140: Delayed Fresnel Tomography
No amplitude measurements
Only phase information
Valid also for dispersive waves
Improved resolution?

## Slide 141: Windows definition
(LTA/STA;
Maggi et al, 2009)
(Wavelet Freq/time;
Lee and Chen, 2013)

## Slide 142: Phases measurements
(Zaroli et al, 2010)

## Slide 143: Workflow for DFT
Taking seismograms
Windowing phases
Picking phases (cross-correlation)
Definition of a misfit function (L2)
Delayed Fresnel Tomography
Model perturbation (velocity)

## Slide 144: Phase differences
(Fichtner et al, 2009)
We do not pick phases as for DFT:

## Slide 145: Full Phases Inversion
(Fichtner et al, 2009)
Do we improve the resolution compared to DFT?
If equivalent, very expensive; if not, smooth transition to FWI

## Slide 146: Workflow for FPI
Taking seismograms
Windowing phases
Definition of a misfit function (time differences)
Full phases inversion
Model perturbation (velocity)

## Slide 147: END HERE

## Slide 148: Another misfit function
Scalar product on D x M
We must minimize
which is related to the possible following factorisation
SVD decomposition if possible : please note that this is a sparse matrice good for tomography

## Slide 149: Tomographic descent
Minimisation of this vector
If one computes
then
Gaussian error distribution of data and of a posteriori model
Easy implementation once Gk has been computed
Extension using Sech transformation (reducing outliers effects while keeping L2 norm simplicity)

## Slide 150: THE Cm-1/2 MATRICE
Shape independent of l
Values depend on l
SATURATION
The matrice Cm has a band diagonal shape
s is the standard error (same for all nodes)
l is the correlation length
n=nx.ny.nz=104 Cm=USUt
(Lanzos decomposition)

## Slide 151: Analysis of coefficients
Values independent of n (n>5000)
Values are only related to s and l
Typical sizes 200x200x50
deduced from 20x20x5 (few minutes)
Strategy of libraries of Cm-1/2 for various l and s=1
Other coefficients could be deduced
R: Cm-1/2 sparse matrice

## Slide 152: An example
l=0.8
sv=100 km/s
sx=100 km
st=100 s
l=0.1
Ray imprints
Same numerical grid for all simulations (either 100x100 or 400x400)
Same results at the limit of numerical precision related to the estimation of the sensitivity matrice

## Slide 153: Illustration of selection {l,sv}
l= 5 km and sv= 3 km/s
Error function analysis will give us optimal values of a priori standard error and correlation length (2D analysis)
sv influence
l influence

## Slide 154: A posteriori information
What is the meaning of the « final » model we provide ?
acceptable

## Slide 155: Probability density
The probability density in the model space is related to the
Data space

## Slide 156: Different informations

## Slide 157: Perspectives
A priori model covariance : location dependent
wavelet decomposition allows local analysis
(work of Matthieu Delost-Geoazur)
Fresnel tomography : introduction of the first Fresnel zone influence in the forward problem
(work of Stéphanie Gautier-Montpellier)

## Slide 158: Kirchhoff approximation
Representation theorem
Kirchhoff summation
Reciprocity

## Slide 164: Born approximation
Single scattering approximation
Surface approximation

## Slide 165
(Forgues et al., 1996)

## Slide 166
(Forgues et al., 1996)

## Slide 167: THANK YOU !
http://seiscope2.osug.fr

## Slide 168: Linearized Inverse Problem
Misfit function
First loop over models : for current model (iteration k)
  Forward problem
    Solve eikonal equation
    Compute synthetic travel-times and delayed times
  Adjoint problem
    Solve adjoint equation
    Build gradient
Descent method (one-step gradient or conjugate gradient or l-BFGS)
Update the model
(Sei & Symes, 1994; Leung & Qian, 2006; Taillandier et al, 2009)
One-loop procedure
Complexity: for forward/adjoint formulation and for gradient

## Slide 169: Linearized Inverse Problem
Misfit function
First loop over models : for current model (iteration k)
  Forward problem
    Solve eikonal equation
    Compute synthetic travel-times and delayed times
  Adjoint problem
    Solve adjoint equation
    Build gradient
Second loop over linear system :
  Truncated Newton method based on iterative conjugate gradient
  (matrix free approach for product , thanks to second-order adjoint formulation)
Update the model (Métivier et al, 2013)
Two-loop procedure
Full Hessian impact is evaluated

## Slide 170: Linearized Inverse Problem
No explicit evaluation of the Hessian :
only products « » and « » are required in LSQR algorithm
Paige & Sanders (1982)
Misfit function
First loop over models : for current model (iteration k)
  Forward problem
    Solve eikonal equation
    Compute rays and synthetic travel-times
  Build sensitivity matrix and delayed times
Second loop over linear system: iteratively solve
using conjugate gradient (LSQR, for example)
Update the model
Two-loops procedure

## Slide 171
Initial velocity model
Eikonal solver (src)
Adjoint solver (src)
Gradient estimation
One loop
End
Linearized Inverse Problem
One-loop procedure
Gradient methods/
Quasi-Newton methods such as l-BFGS method
Storage of previous gradients and models
(Sei & Symes, 1994; Leung & Qian, 2006; Taillandier et al, 2009)

## Slide 172: Linearized Inverse Problem
Misfit function
One-loop procedure
Complexity: for eikonal/adjoint equations
and for gradient estimation
(
Complexity: for eikonal formulation
for back-ray tracing
for storage of sensitivity matrix
Reminder: two-loops procedure

## Slide 173: Forward and adjoint problems
Forward problem based on Eikonal equation
is the travel time field
Adjoint problem based on Transport equation
is the adjoint field
Non-linear PDE: forward
Linear PDE: adjoint

## Slide 174: Reflection configuration
Sources and receivers at the free surface

## Slide 175: Eikonal solver
(Noble et al, 2014)

## Slide 176: Adjoint solver

## Slide 177
Adjoint solver

## Slide 178
Adjoint solver

## Slide 179
Adjoint solver

## Slide 180
Adjoint solver

## Slide 181: Single source gradient

## Slide 182
Gradient comparison

## Slide 183
Comparison between adjoint and frozen-ray approach
Adjoint versus F-ray inversion

## Slide 184
Transmission synthetic example
l-GFGS, PCG, PTCN optimization provide almost same results

## Slide 185
Transmission synthetic example

## Slide 186
Partial Conclusion
Travel-time tomography could be efficiently performed using adjoint approach and l-BFGS optimization – our best choice -
  One-loop procedure
  Low complexity increase
  Better regularization tuning
  (as the sensitivity matrix derivative is not explicitely evaluated)
Requirement of accurate Eikonal solvers: on-going work in collaboration with Mines-Paris Tech group (H. Chauris & M. Noble)
Reduced complexity when considering adjoint formulation: independent of the number of receivers (or sources)
Joint event-velocity multi-parameter inversion is expected to require the Newton method for proper scaling: on-going work.

## Slide 187: Linearized Inverse Problem
No explicit evaluation of the Hessian :
only products « » and « » are required in LSQR algorithm
Paige & Sanders (1982)
Misfit function
First loop over models : for current model (iteration k)
  Forward problem
    Solve eikonal equation
    Compute rays and synthetic travel-times
  Build Fréchet derivative matrix and delayed times
Second loop over linear system: iteratively solve
using conjugate gradient (LSQR, for example)
Update the model
Two-loops procedure

## Slide 188: Linearized Inverse Problem
Misfit function
First loop over models : for current model (iteration k)
  Forward problem
    Solve eikonal equation
    Compute rays and synthetic travel-times
  Build Fréchet derivative matrix and delayed times
Second loop over linear system: iteratively solve
using conjugate gradient (LSQR, for example)
Update the model
Two-loops procedure
Complexity: for forward/adjoint formulation and for gradient storage (: sparsity )

## Slide 189: Linearized Inverse Problem
Misfit function
First loop over models : for current model (iteration k)
  Forward problem
    Solve eikonal equation
    Compute synthetic travel-times and delayed times
  Adjoint problem
    Solve adjoint equation
    Build gradient
Descent method (one-step gradient or conjugate gradient or l-BFGS)
Update the model
(Sei & Symes, 1994; Leung & Qian, 2006; Taillandier et al, 2009)
One-loop procedure
No explicit evaluation of the Hessian
l-BFGS provides an evaluation of the H-1 from previous stored gradients

## Slide 190: Linearized Inverse Problem
Misfit function
First loop over models : for current model (iteration k)
  Forward problem
    Solve eikonal equation
    Compute synthetic travel-times and delayed times
  Adjoint problem
    Solve adjoint equation
    Build gradient
Descent method (one-step gradient or conjugate gradient or l-BFGS)
Update the model
(Sei & Symes, 1994; Leung & Qian, 2006; Taillandier et al, 2009)
One-loop procedure
Complexity: for forward/adjoint formulation and for gradient

## Slide 191: Linearized Inverse Problem
Misfit function
First loop over models : for current model (iteration k)
  Forward problem
    Solve eikonal equation
    Compute synthetic travel-times and delayed times
  Adjoint problem
    Solve adjoint equation
    Build gradient
Second loop over linear system :
  Truncated Newton method based on iterative conjugate gradient
  (matrix free approach for product , thanks to second-order adjoint formulation)
Update the model (Métivier et al, 2013)
Two-loop procedure
Full Hessian impact is evaluated

## Slide 192: Joint hypocenter/velocity
Events at 4.2 km
Random initial hypocenters
Strong trade-off between velocities and hypocenter parameters
- Calibration of weights between these parameters (Spakman & Nolet, 1988; Le Meur et al., 1997)
- Annealing operator (Pavlis and Booker, 1980; Julian and Gubbins, 1980)
Toy example

## Slide 193: Joint hypocenter/velocity
Events at 4.2 km
Random initial hypocenters
Strong trade-off between velocities and hypocenter parameters
- Calibration of weights between these parameters (Spakman & Nolet, 1988; Le Meur et al., 1997)
- Annealing operator (Pavlis and Booker, 1980; Julian and Gubbins, 1980)
Toy example

## Slide 194: Vp/XYZT0 inversion
SVD decomposition of sensitivity matrix
Not scaled
Scaled
Hypocenter parameter
(x,y,z,t0) for each event
Vp parameter on a grid (640 dofs)
Zoom on hypocenter parameters (x,y,z,t0)

## Slide 195: A know example
Simultaneous inversion of velocity and hypocenter parameters (Pavlis & Booker, 1980; Julian & Gubbins, 1980)
Vp velocity and four parameters (x,y,z,t0) for each quake
Le Meur et al (1997)
Hypocenter parameters
In the zoom parameters are ordered as
(x,y,z,t);(x,y,z,t); ….
Scaling is required and was obtained by numerical calibration !

## Slide 196: Vp inversion only
Exact positions
Fixed initial positions

## Slide 197: Vp and XYZ through l-BFGS
Same results with LSQR or TCN …

## Slide 198
Vp and XYZT0 through LSQR
LSQR-like approach
solving the Gauss-Newton equation …
The introduction of the origin time seems to modify dramatically the multi-parameter inversion …

## Slide 199: Vp and XYZT0 through TCN
Only TCN seems to work more efficiently … and turns out to recover both hypocenter parameters (four) and velocity structure …
Expected improvements by preconditioning the normal equation …

## Slide 200: Partial conclusion
Joint inversion of velocity structure and hypocenter parameters presents strong trade-off.
Estimation of the inverse Hessian operator is quite important for mitigating them.
3D real applications will illustrate the importance of considering Hessian effects.